## Slide 1
Multi-User Angle-Domain Beamforming and Non-Orthogonal Multiple Access for Millimeter-Wave Massive MIMO Systems
Doctoral Thesis Defense of
Israa KHALED
Jury Members Prof. Ghaya REKAYA-BEN OTHMAN Prof. Jean-Pierre CANCES Prof. Kosai RAOOF Prof. Chadi ABOU-RJEILY | Telecom Paris Limoges University Le Mans University Lebanese American University
Supervisors Prof. Michel JEZEQUEL Prof. Bachar ELHASSAN Dr. HDR Charlotte LANGLAIS Dr. Ammar EL FALOU | IMT Atlantique Lebanese University IMT Atlantique KAUST

## Slide 2
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Motivation, Contributions
Exponential growth of data traffic
Explosion in the number of connected devices
Appearance of new use cases:
  Massive machine-type communications
  Ultra-reliable low-latency communications
  Enhanced mobile broadband
Requirements
High spectral efficiency
High energy efficiency
Massive connectivity
High Reliability
Ultra-low latency
Source: ITU-R Rec. M.2083
Massive machine type communications
Ultra-reliable and low latency communications
Enhanced mobile broadband
Gigabytes in a second
Smart home/building
Voice
Smart city
3D video, UHD screens
Work and play in the cloud
Augmented reality
Industry automation
Mission critical application
Self driving car
Requirements of Next-Generation Cellular Networks

## Slide 3
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Key Technologies for Next-Generation Cellular Networks
Millimeter-Wave (MmWave) bands
  Frequencies from 24 GHz to 300 GHz
  Large bandwidth available
  Suitable for small cells
Massive multiple-input multiple-output (MIMO)
  Large number of antennas
  High beamforming gains
  High spectral and energy efficiencies
  High reliability
Non orthogonal multiple access (NOMA)
  Exploits non-orthogonal resources, e.g., power domain
  Serves multiple users at the same orthogonal resources
  Manages massive connectivity
Motivation, Contributions

## Slide 4
Beamforming
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Motivation, Contributions
Multi-User (MU) MIMO Systems for MmWave Downlink Transmissions
MU-MIMO beamforming (BF)
  Requires prior channel knowledge
  Multiplexes data streams at each antenna
  Improves received power
  Reduces inter-user interference
Users’ number
Antennas’ number
BF with mmWave massive MIMO
  High channel estimation overhead
  High implementation complexity
  High cost
Need to adopt with mmWave massive MIMO low-complex BF techniques requiring partial channel state information (CSI)
Figure: Downlink MU-MIMO system

## Slide 5
I. Angle-domain digital beamforming for mmWave MIMO systems
II. Angle-domain MIMO-NOMA for mmWave communications
III. Angle-domain hybrid beamforming and NOMA for mmWave massive MIMO systems
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Motivation, Contributions
Interest of angle-domain information (ADI) as a partial CSI for mmWave downlink MIMO systems?
NOMA cluster
High inter-user interference
Hybrid beamforming: Trade-off
Performance
Complexity
Cost
Power consumption
Narrow beams
Limited radio-frequency (RF) chains
____________________________
Lack in degrees of freedom
User’s angle
Digital phase shifters

## Slide 6
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Part I
Angle-Domain Digital Beamforming for MmWave Massive MIMO Systems

## Slide 7
Introduction, Channel and System Models, Summary
Angle-domain digital BF (AD-DBF)
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
AD-DBF [1]
Requires users’ angles
Adopts digital phase shifters
Steers a beam toward each user
AD-DBF Characteristics
Low implementation complexity
Low channel feedback rate
Angle-domain information (ADI) [2]
Slowly time-varying CSI
Does not scale with the antennas’ number
What about the performance of AD-DBF in mmWave environments and with large-scale antenna arrays (LSAAs)?
[1] A. Roze, “Massive mimo, une approche angulaire pour les futurs systèmes multiutilisateurs aux longueurs d’onde millimétriques,” Ph.D. dissertation, INSA de Rennes, 2016.
Figure: Illustration of AD-DBF in downlink.

## Slide 8
[1] M. K. Samimi and T. S. Rappaport, “3-D millimeter-wave statistical channel model for 5G wireless system design,” IEEE Trans. Microw. Theory Tech.,, 2016.
NYUSIM is a MATLAB-based open-source simulator developed by New York University [1]
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
New York University Simulator (NYUSIM)
Introduction, Channel and System Models, Summary
100 m
LoS path
LoS path
NYUSIM
Implements the statistical spatial channel model (SSCM)
Uses the time-cluster and spatial lobe approach
Cell Radius | 100 m
Carrier frequency, f | 28 GHz
Environment scenario | LoS
LoS (line-of-sight)
Simulated Angle Power Spectrum in Rural Scenario.
Simulated Angle Power Spectrum in Urban Scenario.
Output figures generated by NYUSIM

## Slide 9
System Model
  Received signal vector
  System sum-rate
      SINR at UE k
Channel Matrix of all UEs
Normalization BF Factor
Channel Model
  Channel vector between the BS and UE k
      : Array steering vector for to the -th path in UE ‘s channel
Number of paths
Introduction, Channel and System Models, Summary
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Downlink MU-MIMO System
  One base station (BS)
  antennas ( horizontal antennas, vertical antennas)
  Digital beamforming (DBF)
  K single-antenna user equipments (UEs)
SMOTE
Complex gain of the corresponding path
Azimuth angle
Elevation angle
    All the channel coefficients are generated using NYUSIM
BF Matrix of all UEs
Signal-to-interference plus noise ratio
Symbols Vector of all UEs
Figure: MU-MIMO system model
Figure: Downlink MU-MIMO system.

## Slide 10
Multi-path environment:
  SINR achieved at UE
Mono-path environment:
  SINR achieved at UE
Introduction, Channel and System Models, Summary
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Performance of AD-DBF in Mono- and Multi-Path environments
Inter-user interference term
Lack in diversity of non-LoS (NLoS) paths
Interference from the LoS beams of other UEs
AD-DBF generates a beam at the user’s direction, i.e., the LoS path’s direction
Beamforming matrix
Array steering vector of the LoS path of each user

## Slide 11
Introduction, Channel and System Models, Summary
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Summary
AD-DBF is an appealing BF technique for mmWave massive MIMO systems
Is a trade-off performance, complexity and channel estimation overhead
Is more suitable for highly LoS environments
Compensates with massive antennas the lack in the diversity of NLoS paths
Work publications
I. Khaled, A. El Falou, C. Langlais, B. ElHassan, and M. Jezequel, “Multi-user digital beamforming based on path angle information for mm-wave MIMO systems,” in Proc. International ITG Workshop on Smart Antennas (WSA), Feb. 2020.
I. Khaled, A. El Falou, C. Langlais, B. ElHassan, and M. Jezequel, “Performance evaluation of linear precoding mmWave multi-user MIMO systems with NYUSIM channel simulator,” in 2019 2nd IEEE Middle East and North Africa COMMunications Conference (MENACOMM). IEEE, 2019.
Baseline: Conjugate beamforming
  Requires the whole channel
  Maximizes the BF gain at the desired user
Scenario: Rural and urban environments
MmWave channel model: SSCM implemented by NYUSIM
Performance metric: Sum-rate

## Slide 12
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Part II
Angle-Domain MIMO-NOMA for MmWave Communications

## Slide 13
How to reduce interference without deploying additional antennas?
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions
Contributions
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
AD-DBF issue
UEs located at the same direction  high inter-user interference  low data rate
Degradation of the AD-DBF performance
AD-DBF Limitation
AD MIMO-NOMA
Solution
Implementing massive antennas
DBF issues with massive MIMO
Complexity
Cost
Channel estimation overhead
Power-domain NOMA (PD-NOMA)
Adopts superposition coding at the transmitter
Adopts successive interference cancellation (SIC) at the receiver
Serve multiple users non-orthogonally on the same orthogonal resource
Allocate different power levels to the multiplexed users

## Slide 14
State-of-Art
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
MIMO-NOMA in the literature
Most of them adopt
  Full CSI (FCSI)
  High complex precoder
Few works adopt the statistical CSI [1]
Recent works [2-3]
  Exploit the directionality of mmWave transmissions
  Adopt angle or both distance and angle
Limitations
AD user clustering (UC) uses angular distance
Lack of MIMO-NOMA design with only ADI
Next UP: AD MIMO-NOMA
Exploit the features of mmWave transmissions
Derive new angular-based metrics
Propose new user ordering, user clustering and power allocation techniques using only ADI
[1] J. Choi, “Joint rate and power allocation for NOMA with statistical CSI,” IEEE Trans. Commun., vol. 65, no. 10, pp. 4519–4528, 2017.
[2] E. M. Mohamed, “Joint users selection and beamforming in downlink millimetre-wave NOMA based on users positioning,” IET Communications, 2020.
[3] X. Lu et al., “A joint angle and distance based user pairing strategy for millimeter wave NOMA networks,” in Proc. WCNC, 2020.
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions

## Slide 15
Power allocation coefficient
AD MIMO-NOMA
  K UEs
  C spatial clusters: NOMA clusters and SU clusters
  UEs exists in the c-th cluster.
  NOMA is performed in the c-th cluster if >1.
System Model
  Received signal at
  : Array steering vector for the c-th cluster angle
Data Transmission
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Channel vector between BS and
Normalization BF factor
BF weight vector corresponding to the c-th cluster
Superposed signal of the c-th cluster
Desired signal of
Power allocated to the c-th cluster
Figure: Angle-domain (AD) MIMO-NOMA
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions

## Slide 16
  After SIC: Received signal at
  Channel quality at : Superposed signal to other-clusters interference plus noise ratio
  Optimal user ordering strategy:
  Efficient SIC constraint:
  Sum-Throughput:
Data Transmission
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Channel vector between BS and
Normalization BF factor
Desired signal
Intra-cluster interference
Inter-cluster interference
Bandwidth
MIMO-NOMA
Optimal user ordering strategy requires FCSI
Efficient SIC constraint requires FCSI
User clustering and power allocation techniques maximizing require FCSI
Need to design user ordering, user clustering and PA techniques with only ADI
SU clusters
NOMA clusters
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions
Figure: Angle-domain (AD) MIMO-NOMA
Notes: After SIC, the received signal is given by this equation
** where the first term is the desired signal,
** the second is the intra-cluster interference and ** the third one is inter-cluster interference.
** The channel quality denoted as zeta represents the superposed signal to other clusters interference plus noise ratio and is given by this equation.
** Thus, the optimal user ordering strategy is that sorts the PA coefficients in the ascending order of their channel qualities.
** SIC works properly only if the power allocation coefficients satisfy the following condition, where 𝑃min is the minimum power difference between users to allow efficient SIC decoding.
** The Optimal User Ordering Strategy and the Efficient SIC constraint depends on zeta
** which requires FCSI. Therefore, they requires also FCSI.
** The sum-throughput within
** the bandwidth B can be expressed as a function of zeta
** the first term is the sum-throughput of SU clusters and
** the second is that of NOMA clusters.
**Thus, any user clustering and PA techniques maximizing 𝑅_𝑇 requires FCSI.
** However, FCSI is difficult to obtain in practice, so there is a need to design user clustering and ordering and PA techniques with only the knowledge of ADI.
__________________________________
In other words, NOMA allocate high power to the weak users.

## Slide 17
MmWave Channel Model
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
MmWave channel vector
MmWave channel’s properties [1]
Simplifying assumption
NLoS paths (q>1) are very attenuated w.r.t. LoS path (q=1)
High directional propagation
High sensitivity to blockage
[1] M. R. Akdeniz, et al, “Millimeter wave channel modeling and cellular capacity evaluation,” IEEE J. Sel. Areas in Commun., 2014.
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions

## Slide 18
ADI-based Channel Quality and Sum-Throughput Metrics
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
High signal-to-noise ratio (SNR) regime
User Ordering Strategies with Partial CSI in the Literature
Distance from the BS [1]
Large-scale fading coefficients [2]
Effective channel gains [3]
These strategies
requires additional channel overhead to ADI
Does not consider the inter-cluster interference
: ADI-based channel quality metric
ADI-based user ordering strategy:
ADI-based user ordering strategy:
Requires only ADI
Considers inter-cluster spatial interference
depends on
Users’ angles
Intra- and inter-cluster powers
ADI-based Channel Quality:
User ordering strategy in the literature
Effective channel gain [1]
Distance from the BS [2]
Large-scale fading coefficients [3]
ADI-based Sum-Throughput:
[1] X. Hu, et al “Angle-domain mmWave MIMO NOMA systems: analysis and design,” in Proc. IEEE ICC, 2019.
[2] Z. Ding, P. Fan, and H. V. Poor, “Random beamforming in millimeter-wave NOMA networks,”IEEE Access, 2017.
[3] M. Morales-Céspedes, et al., “Semi-blind interference aligned NOMA for downlink MU-MISO systems,” IEEE Trans. Commun., 2019.
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions

## Slide 19
ADI-based Inter-User Spatial Interference Metric
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
AD user clustering in the literature
Most of them use the angular distance
  UC can only be applied with uniform linear array (ULA)
  does not describe properly inter-user interference
  Interference also depends on beamwidth
ADI-based Inter-User Spatial Interference Metric
number of antennas
array steering vector of LoS path in UE k channel
array steering vector of the beam generated toward UE u spatial direction
Figure: Illustration of the normalized array factor of beam pointed at with the LoS path of UE k at
Determines the level of inter-user spatial interference using only ADI
Includes both angular distance and beam-width information
With , a unique threshold can be defined whatever the antennas number and users’ angles.
Definition: The beamwidth is defined as the angular distance - | satisfying
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions
Notes: Most of the existing AD user clustering algorithms use the angular distance. Thus, these algorithms can only be applied to ULA. Moreover, Δ𝜃 is not enough to describe properly inter-user interference, which also depends on the beamwidth. It’s worth noting that the beamwidth depends on the antennas’ number and the steering angle. To this end, we define the following ADI-based Inter-User Spatial Interference Metric, where M is the number of antennas, a𝐻1,𝑘 is the array steering vector of the LoS path in UE 𝑘 channel, and a1,𝑢 is the array steering vector of the beam generated toward UE 𝑢 spatial direction. We find that beta_k,u represents the normalized antenna array factor. To illustrate this relation, we depict in blue the normalized array factor of the beam pointed toward UE 𝑢 and the corresponding value of 𝛽𝑘,𝑢. It can be seen that 𝛽 is an important metric to determine the level of inter-user spatial interference using only the users’ angles, and that beta includes both angular distance and beam-width information. The〖 𝛽〗_0 beamwidth is defined as the angular distance such that the normalized array factor is equal to beta 0. Therefore. with 𝜷_(𝑘,𝒖), a unique threshold 𝛽_0 can be defined whatever the number of antennas or the users’ angle.

## Slide 20
2-User and Multi-User Clustering (UC) Algorithms
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
2-User and Multi-User Clustering Algorithms
Use the definition
Can be applied with any uniformly excited array architecture
Initialize an inter-user interference threshold
2-user UC: groups 2-by-2 the users with high interference in the same cluster.
Multi-user UC: groups all users having interference with each others in the same cluster.
Figure: Illustration of the normalized array factor of the beams pointed at UE u with
Lemma1:
UE k, having > is located in the -width of the main lobe of the UE u beam, only if >
First side lobe (FSL) level
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions
[1] H. J. Visser, Array and phased array antenna basics. Wiley Online Library, 2005.
Notes: In this lemma, we prove that user k having beata k u larger than beta 0 is located in the beta 0 width of the main lobe of the UE u beam only if beta0 is larger than 0.217 which is the first side lobe level. The figure on the right can be easily illustrates this lemma. It’s worth noting that this value doesn’t depend on the users number and the steering angle. Using the beta definition, we propose 2-user and multi-user clustering algorithms that can be applied with any uniformly excited antenna array architecture. First of all, we initialize the inter-user interference threshold 𝛽_0. The groups 2-by-2 the users with high inter-user interference, i.e., 𝛽≥𝛽_0, in the same NOMA cluster. Moreover, we generalize to the case of multi-user and we develop a Multi-user UC algorithm that groups all users having interference with each others, i.e., 𝛽≥𝛽_0, in the same NOMA cluster.

## Slide 21
type =ADI or FCSI
Intra-cluster PA constraint
Total power constraint
Efficient SIC constraint
Non-convex Problem
Intra- and Inter-Cluster Power Allocation (PA)
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Karush-Kuhn-Tucker (KKT) conditions
Fixed Inter-Cluster PA
Intra- and Inter-Cluster PA Optimisation Problem
Closed-Form Intra-Cluster PA: KKT-PA
Intra-Cluster PA Optimisation Problem
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions
Notes: (P1) maximizes the system sum-throughput by jointly optimizing the intra-cluster PA 𝜸=\{𝛾_(𝑙,𝑐), ∀ 𝑙,𝑐} and inter-cluster PA 𝒑={𝑝_𝑐, ∀𝑐} strategies..
The PA factors 𝜸 and 𝒑 from different UEs are very coupled in (P1)
To obtain closed-form solutions, we apply a fixed inter-cluster PA  (P1) is reformulated as an intra-cluster PA maximization problem subject to the intra-cluster PA and efficient SIC constraints as follows
In multi-user MIMO-NOMA scheme, the number of UEs per cluster is variable.
We allocate a power 𝑝_𝑐 to the c-th cluster proportional to the number Kc of UEs served in the c-th cluster to guarantee a certain power fairness among UEs.

## Slide 22
 | Number of real coefficients per channel estimation for each UE
2-user or multi-user AD MIMO-NOMA with ADI | (=1 if ULA or =2 if URA)
2-user or multi-user AD MIMO-NOMA with FCSI | 
 | Number of real coefficients per channel estimation for each UE
2-user or multi-user AD MIMO-NOMA with ADI | 
2-user or multi-user AD MIMO-NOMA with FCSI | 
The proposed NOMA protocol using ADI has a significant sum-rate in highly directional mmWave environments
2D AD MIMO-NOMA: Spectral Efficiency
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Figure: Average system spectral efficiency versus the total number of users, 𝐾, with = 0.5.
Number of antennas, M | 32
Carrier frequency, f | 28 GHz
System Bandwidth, B | 20 MHz
Cell Radius | 100 m
Transmission Power, | 30 dBm
Noise Power, | -101 dBm
 | 1 mW
Number of paths in rural environment according to NYUSIM | {1,2}
Number of antennas, M | 32
Carrier frequency, f | 28 GHz
System Bandwidth, B | 20 MHz
Cell Radius | 100 m
 | 30 dBm
 | -101 dBm
 | 1 mW
Number of paths in rural environment according to NYUSIM | {1,2}
Table: Simulation parameters
ADI: angle-domain information
FCSI: full channel state information
Uniform linear array (ULA)
AD MIMO-NOMA with FCSI NOMA
  𝛽-based user clustering
  FCSI-based user ordering
  FCSI-based power allocation
AD MIMO-NOMA with ADI NOMA
  𝛽-based user clustering
  ADI-based user ordering
  ADI-based power allocation
AD MIMO-OMA
  2 user 𝛽-based user clustering
  Equal resource allocation
AD MIMO-NOMA with FCSI
VS
AD MIMO-NOMA with ADI
AD MIMO-NOMA
VS
AD MIMO-OMA
NOMA exploits multi-user diversity unlike OMA
36%
AD MIMO-NOMA
VS
AD-DBF
AD-DBF can not support more than users
AD MIMO-NOMA manages massive connectivity
Table: Number of real coefficients per channel estimation for each UE
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions
FCSI
ADI
FCSI
ADI
OMA
NOMA
32
AD-DBF

## Slide 23
3D AD MIMO-NOMA: Spectral Efficiency and Energy Efficiency
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Figure: Average system spectral and energy efficiencies for 2-user and multi-user AD MIMO-NOMA using URA with 𝑀𝑥 = 32 and 𝑀𝑧 = 2 and for C-AD-DBF using URA with 𝑀𝑥 = 32 and 𝑀𝑧 = {2, 4, 5, 6} in a rural environment.
Energy efficiency (EE)
170%
129%
𝜌 = 0.4, = 1𝑊 and = 10𝑊 [1]
2-user AD MIMO-NOMA with
AD-DBF with
VS
Multi-user AD MIMO-NOMA with
AD-DBF with
VS
AD MIMO-NOMA is an alternative solution to reduce interference without increasing the antennas number??
Uniform rectangular array (URA)
Inefficiency of power amplifiers
Emitted power
Basic power
Power consumption per antenna
[1] E. Björnson et al., “Massive MIMO networks: Spectral, energy, and hardware efficiency,” Foundations and Trends in Signal Processing, 2017.
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions
AD MIMO-NOMA is an alternative solution to reduce interference without increasing the antennas number
✔
 | Number of horizontal antennas, | Number of vertical antennas,
2-user or multi-user AD MIMO-NOMA | 32 | 2
AD-DBF | 32 | {2,4,5,6}
2-user or multi-user AD MIMO-NOMA | 32 | 2
AD-DBF | 32 | {2,4,5,6}

## Slide 24
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Work publications:
I. Khaled, C. Langlais, A. El Falou, B. Elhassan, M. JEZEQUEL, "Multiuser Angle-domain MIMO-NOMA System For Mmwave Communications", IEEE Access, 2021, Vol. 9, P. 129443-129459.
I. Khaled, C. Langlais, A. El Falou, M. Jezequel, B. ELHASSAN, "Joint SDMA And Power-domain NOMA System For Multi-user Mmwave Communications", 2020 International Wireless Communications And Mobile Computing (IWCMC). IEEE, 2020.
Derive angular-based metrics
Propose 2-user and multi-user AD MIMO-NOMA schemes
  AD MIMO-NOMA significantly reduce interference and manage massive connectivity without deploying additional antennas
  ADI-based user ordering strategy outperforms the existing strategies with limited feedback
  ADI-based power allocation allows for efficient SIC
Conclusions
Introduction, AD MIMO-NOMA System Description, ADI-based Performance Metrics, User Clustering, Power Allocation, Simulation Results, Conclusions

## Slide 25
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Part III
Angle-Domain Hybrid Beamforming-based MmWave Massive MIMO-NOMA

## Slide 26
Introduction, System Model, Joint 𝛽-based SB-NOMA and TDMA, Joint Angle-Domain SB- and MB-NOMA, Simulation Results, Conclusions
Contribution
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
AD massive MIMO-NOMA
AD MIMO-NOMA Single-beam (SB)-NOMA
DBF requires as many RF chains as antennas
Objective: Increase the BF gain by using hundreds of antennas
AD HBF-based massive MIMO-NOMA
Limited RF chains
Narrow beams
 Lack in Degrees of Freedom (DoFs)
How to offer additional DoFs in such systems??
Narrow beams with LSAAs
DBF with massive MIMO
High complexity
High cost
High power consumption
Trade-off performance, complexity, cost, and power consumption
Hybrid beamforming (HBF)

## Slide 27
Introduction, System Model, Joint 𝛽-based SB-NOMA and TDMA, Joint Angle-Domain SB- and MB-NOMA, Simulation Results, Conclusions
State-of-Art
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
AD HBF-based massive MIMO-NOMA in the Literature
Next UP: AD HBF-based massive MIMO-NOMA
Our proposed schemes
  Can be applied with both ULA and URA
  Require only ADI
Limitations
[1] and [2] apply only with ULA
[2] utilizes FCSI to design resource allocation techniques
[1] X. Hu, et al “Angle-domain mmWave MIMO NOMA systems: analysis and design,” in Proc. IEEE ICC, 2019.
[2] Z. Wei, et al “Multi-beam NOMA for hybrid mmWave systems,” IEEE Trans. Commun., 2018.
  Exploits the Time Division Multiple Access (TDMA) technique.
  Proposes a group clustering algorithm in time domain using the angular distance
  Designs a multi-beam (MB) NOMA framework to serve users with arbitrary angles using NOMA.
  Proposes a beam splitting technique to generate multiple beams at the same RF chains
Angle-domain mmWave MIMO NOMA systems: analysis and design [1]
The use of TDMA with NOMA imposes more signal processing and synchronization complexity.
Multi-beam NOMA for hybrid mmWave systems [2]

## Slide 28
Introduction, System Model, Joint 𝛽-based SB-NOMA and TDMA, Joint Angle-Domain SB- and MB-NOMA, Simulation Results, Conclusions
System Model and Problem Formulation
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
AD HBF-based massive MIMO-NOMA:
  A BS with antennas and RF chains
  users
  HBF with fully connected structure
  Pure analog precoder, i.e.,
  The K users are clustered within SU groups and SB-NOMA groups
Problem Formulation:
  Overloaded scenario:
  The spatial and power domains are not sufficient to serve all users
  Need to leverage new degrees of freedom!!!
Proposed schemes:
  Joint SB-NOMA and TDMA scheme
  Joint SB and MB-NOMA schemes
HBF matrix:
Number of total groups
Figure: HBF-based SB-NOMA-MIMO scheme.

## Slide 29
Introduction, System Model, Joint 𝛽-based SB-NOMA and TDMA, Joint Angle-Domain SB- and MB-NOMA, Simulation Results, Conclusions
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
-based Time-domain Group Clustering Algorithm
Two-stage algorithm inspired from [1]
Uses the definition
Apply with any uniformly excited array architecture
X. Hu, et al. 2019 [1]
Uses angular distance
Only applies with ULA
Start: K users
-based multi-user UC
SB-NOMA groups
single-user groups
End
-based Time-Domain Group Clustering Algorithm
YES
NO
Time-domain
…
TS
TS
TS
1st Stage
2nd Stage
Minimize inter-group interference in each time-slot
The groups having highest inter-group interference
The (- ) remaining groups
: Number of time-slots
[1] X. Hu, et al. “Angle-domain mmWave MIMO NOMA systems: analysis and design,” in Proc. IEEE ICC, 2019.
-based Time-domain Group Clustering Algorithm
Initialisation: ,
: Inter-group interference
TDMA with NOMA imposes more signal processing and synchronization complexity.
User and Group Clustering Algorithms in Space-, Power-, and Time-Domains
Flowchart Diagram

## Slide 30
Figure: Vertically array splitting technique with URA
Introduction, System Model, Joint 𝛽-based SB-NOMA and TDMA, Joint Angle-Domain SB- and MB-NOMA, Simulation Results, Conclusions
Multiple Analog Beams Using Beam Splitting
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Divided by two
Two beams at (, ) and (, ) via beam splitting
Single beam at (, )
Figure: Normalized array pattern response of a single beam and of two beams generated using beam splitting when the BS adopts URA
MB-NOMA framework
  Adopts beam-splitting
  Serves users with arbitrary angles using NOMA at the same RF chain
Beam-splitting with URA
  2-user MB-NOMA groups
  RF chain serves user and user via beam splitting
   The analog beamformer :
user
user
user
user
Figure: 2-user MB-NOMA: Two users served at the same RF chain.
Notes: Now, i will present the beam splitting technique that we extend to deal also with URA. The array steering vector is a function of the steering angle, and the numbers of horizontal and transmit antennas. First, we divide vertically the antenna array into two subarrays, as illustrated in the right figure. By rewritten the array steering vector, we find that the array that generates a beam toward the theta angle can be seen as an array divided into two subarrays and each one generates a beam in the theta direction, where the phase shift between the first and the second subarray is constant. Throughout our study, we consider 2 users in MB NOMA cluster.Assume that RF chain 𝑔 serves user 𝑘 and user 𝑘^′ using NOMA and the beam splitting technique thereby the RF analog beamformer 𝒘_𝑔 is given by this equation, where MX sa is the nb of horizontal antennas per subarray and MzSA is the nb of vertical antennas per subarray. It’s clear that it’s clear that the first subarray can successfully form a beam toward the user 𝑘. Besides, since we add the same phase shift to all the antenna elements in the second subarray that have different phased weights to point a beam toward user k′ . Thereby, the second subarray can also successfully form a beam toward the user 𝑘′.
IN the right, we plot the normalized array pattern responses of a single beam and of two beams generated via beam splitting. Compared to the single
Beam, the maximum magnitude of the main beam response of the two beams is divided by two, i.e., the number of subarrays. This is because the two subarrays have the same dimensions.

## Slide 31
Figure: Sum-rate against Δ𝜃 with 128 × 1 ULA
 3-dB beamwidth
Step 1: Cluster first the users with high spatial interference within SB-NOMA groups
Step 2: Cluster the remaining users within MB-NOMA groups
The 2 beams generated by MB-NOMA are superimposed  SB-NOMA  MB-NOMA.
1
SB-NOMA slightly outperforms MB-NOMA
2
SB-NOMA performance degrades as  due to the severe beam misalignment.
3
MB-NOMA outperforms SB-NOMA and has approximately a constant sum-rate
4
3
4
1
2
Introduction, System Model, Joint 𝛽-based SB-NOMA and TDMA, Joint Angle-Domain SB- and MB-NOMA, Simulation Results, Conclusions
2-User Scenario: SB-NOMA vs MB-NOMA
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
MB-NOMA
SB-NOMA

## Slide 32
Introduction, System Model, Joint 𝛽-based SB-NOMA and TDMA, Joint Angle-Domain SB- and MB-NOMA, Simulation Results, Conclusions
System model
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Figure: Joint SB- and MB MIMO-NOMA scheme.
Joint SB- and MB-NOMA scheme
SU groups
SB-NOMA groups
MB-NOMA groups
System Model
The analog beamformer related to group
Notes: The transmit RF beamformer 𝒘_𝑔 related to group 𝑔 depends on its type and is given by

## Slide 33
Reduces the active RF chains number
Applies MB-NOMA in sparse and overloaded scenarios
Start: K users
-based multi-user UC
SB-NOMA groups
single-user groups
End
2-user MB-NOMA UC
YES
NO
Start: K users
-based multi-user UC
SB-NOMA groups
single-user groups
End
2-user MB-NOMA UC
SB-NOMA groups
MB-NOMA groups
single-user groups
SB-NOMA groups
MB-NOMA groups
single-user groups
Introduction, System Model, Joint 𝛽-based SB-NOMA and TDMA, Joint Angle-Domain SB- and MB-NOMA, Simulation Results, Conclusions
Proposed Schemes
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
SB-MB-NOMA scheme
SB-MB-NOMA-RRFC scheme
Maximizes spectral efficiency
Applies MB-NOMA in overloaded scenarios

## Slide 34
Introduction, System Model, Joint 𝛽-based SB-NOMA and TDMA, Joint Angle-Domain SB- and MB-NOMA, Simulation Results, Conclusions
Simulation Results
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
[1] X. Hu, et al. “Angle-domain mmWave MIMO NOMA systems: analysis and design,” in Proc. IEEE ICC, 2019.
Uniform linear array (ULA) with antennas
AD HBF-TDMA-SB-NOMA [1]
Figure: Sum-rate per time-slot versus the number of users.
DBF:
HBF:
Enable the communication for
Proposed schemes
83%
[1] only applies with ULA
𝛽-HBF-SB-NOMA-TDMA applies with any uniformly excited array architecture
: SB-MB-NOMA outperforms AD-DBF with very few RF chains
66%
[1]
DBF SB-NOMA
SB-MB-NOMA-RRFC
SB-MB-NOMA
AD-DBF
𝛽-SB-NOMA-TDMA
TDMA with NOMA imposes more signal processing and synchronization complexity
Joint SB- and MB-NOMA schemes
    SB-MB-NOMA
    SB-MB-NOMA-RRFC
Notes: We consider a BS adopting a ULA array with 128 antennas. And, we compare our proposed schemes with the existing one that exploits TDMA, and with AD-DBF and the scheme based on DBF proposed in the second part of our study and denoted here as AD DBF SB-NOMA. The DBF schemes requires RF chains as many as antennas, while the HBF –based schemes require a number of RF chains lower or equal to M. Here, we fix this number to 20. Interestingly, All the proposed schemes enable the communication in an overloaded cell when the 𝑛𝑢𝑚𝑏𝑒𝑟 𝑜𝑓 𝑢𝑠𝑒𝑟𝑠 𝑖𝑠 larger than that of RF chains. Besides, in a sparse cell, SB-MB-NOMA outperforms AD-DBF with times less RF chains
Sparse cell:
Congested cell: All proposed schemes enable the connectivity of all users when K>N_RF, while HBF-based SB-NOMA can not.
TDMA
SB-MB-NOMA

## Slide 35
Introduction, System Model, Joint 𝛽-based SB-NOMA and TDMA, Joint Angle-Domain SB- and MB-NOMA, Simulation Results, Conclusions
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Figure: Number of active RF chains per time-slot versus number of users.
[1] X. Hu, et al. “Angle-domain mmWave MIMO NOMA systems: analysis and design,” in Proc. IEEE ICC, 2019.
Uniform linear array (ULA) with antennas
AD HBF-TDMA-SB-NOMA [1]
[1]
SB-MB-NOMA-RRFC
SB-MB-NOMA
𝛽-SB-NOMA-TDMA
TDMA with NOMA imposes more signal processing and synchronization complexity
Joint SB- and MB-NOMA schemes
  SB-MB-NOMA
  SB-MB-NOMA-RRFC
Notes: We consider a BS adopting a ULA array with 128 antennas. And, we compare our proposed schemes with the existing one that exploits TDMA, and with AD-DBF and the scheme based on DBF proposed in the second part of our study and denoted here as AD DBF SB-NOMA. The DBF schemes requires RF chains as many as antennas, while the HBF –based schemes require a number of RF chains lower or equal to M. Here, we fix this number to 20. Interestingly, All the proposed schemes enable the communication in an overloaded cell when the 𝑛𝑢𝑚𝑏𝑒𝑟 𝑜𝑓 𝑢𝑠𝑒𝑟𝑠 𝑖𝑠 larger than that of RF chains. Besides, in a sparse cell, SB-MB-NOMA outperforms AD-DBF with times less RF chains
Sparse cell:
Congested cell: All proposed schemes enable the connectivity of all users when K>N_RF, while HBF-based SB-NOMA can not.
TDMA
SB-MB-NOMA

## Slide 36
Introduction, System Model, Joint 𝛽-based SB-NOMA and TDMA, Joint Angle-Domain SB- and MB-NOMA, Simulation Results, Conclusions
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Work publications:
  I. Khaled, C. Langlais, A. El Falou, B. El Hassan, and M. Jezequel, “Joint single- and multi-beam angle-domain NOMA for hybrid mmWave MIMO systems,” published in WSA 2021; 25th International ITG Workshop on Smart Antennas. VDE, 2021.
  I. Khaled, A. El Falou, C. Langlais, B. El Hassan, and M. Jezequel, “Angle-domain hybrid beamforming-based mmWave massive MIMO-NOMA systems, to be submitted
Design a joint SB-NOMA and TDMA scheme that can be applied with any uniformly excited array architectures
Design joint SB- and MB-NOMA schemes, in which NOMA exploits the multi-user diversity whatever the cell’s load and users’ positions.
  One enhances the spectral efficiency
  The other reduces the active RF chains, i.e., power consumption
The proposed schemes require only ADI

## Slide 37
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Conclusions and Future Works

## Slide 38
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
AD MIMO-NOMA to manage massive connectivity in congested cells
  Derive new angular-based metrics
  Design new user ordering, user clustering and power allocation techniques in angle-domain for the NOMA protocol
AD HBF-based massive MIMO-NOMA to restrict the limitation of SB-NOMA in overloaded scenarios
  Design a joint SB-NOMA and TDMA scheme for any uniformly excited array architecture
  Design joint SB- and MB-NOMA schemes using only NOMA
Conclusions, Future works, List of Publications
Angle-domain information (ADI) is a promising partial CSI for mmWave massive MIMO-NOMA systems

## Slide 39
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Short Term
  Develop an iterative sub-optimal inter-cluster power allocation with ADI
  Develop an angle error model
  Consider the imperfection and the complexity of SIC decoding
Long Term
  AD massive MIMO-NOMA systems in uplink mmWave transmissions
  Effective resources allocation for joint single and multi-beam NOMA schemes
  AD MIMO-NOMA with OFDM in wideband mmWave channels
Conclusions, Future works, List of Publications

## Slide 40
Journal Papers:
I. KHALED, C. LANGLAIS, A. EL FALOU, B. ELHASSAN, M. JEZEQUEL, "Multiuser angle-domain MIMO-NOMA system for mmWave communications", IEEE Access, 2021, vol. 9, p. 129443-129459.
I. KHALED, A. EL FALOU, C. LANGLAIS, B. ELHASSAN, M. JEZEQUEL, "Angle-domain hybrid beamforming-based mmWave massive MIMO-NOMA systems", submitted
Conference Papers:
I. KHALED, C. LANGLAIS, A. EL FALOU, M. JEZEQUEL, B. ELHASSAN, "Joint Single-and Multi-beam angle-domain NOMA for hybrid mmWave MIMO systems", WSA 2021; 25th International ITG Workshop on Smart Antennas. VDE, 2021.
I. KHALED, C. LANGLAIS, A. EL FALOU, M. JEZEQUEL, B. ELHASSAN, "Joint SDMA and power-domain NOMA system for multi-user mmWave communications", 2020 International Wireless Communications and Mobile Computing (IWCMC). IEEE, 2020.
I. KHALED, A. EL FALOU, C. LANGLAIS, B. ELHASSAN, M. JEZEQUEL, "Multiuser digital beamforming based on path angle information for mmWave MIMO systems“ WSA 2020; 24th International ITG Workshop on Smart Antennas. VDE, 2020.
I. KHALED, A. EL FALOU, C. LANGLAIS, B. ELHASSAN, M. JEZEQUEL, "Performance evaluation of linear precoding mmWave multi-user MIMO systems with NYUSIM channel simulator", 2019 2nd IEEE Middle East and North Africa COMMunications Conference (MENACOMM). IEEE, 2019.
Part I: AD-DBF
Part II: AD MIMO-NOMA
Part III: AD HBF-based massive MIMO-NOMA
Discussion
Introduction
Conclusions, Future works, List of Publications